## Slide 1
CAN(Controller Area Network) Protocol

## Slide 2: Introduction
Originally developed by Robert Bosch for automobile in-vehicle network in the 1980s
Multi-master, Broadcasting, Serial communication protocol
Priority-based bit-wise arbitration
For reliable and Robust data exchange between ECUs especially in noisy environments
Cost effective, Compact and fast
It is a message-based protocol. ie, there are no defined addresses, just defined messages.

## Slide 5: CAN Characteristics
All messages are broadcast
Any node is allowed to broadcast a message
Each message contains an ID that identifies the source or content of a message
Each receiver decides to process or ignore each message

## Slide 6
Logic 1 is a recessive state. To transmit 1 on CAN bus, both CAN high and CAN low should be applied with 2.5V.
Logic 0 is a dominant state. To transmit 0 on CAN bus, CAN high should be applied at 3.5V and CAN low should be applied at 1.5V.
The ideal state of the bus is recessive.
If the node reaches the dominant state, it cannot move back to the recessive state by any other node.

## Slide 7
The maximum number of nodes is not specified.
Networks are limited by electrical loading, up to 64 nodes is normal

## Slide 8: CAN data rate
Bit Rate I Bus Length
1M bit/sec 500K bit/sec 250K bit/sec 125K bit/sec
40 meters (131 feet)
100 meters (328 feet)
200 meters (656 feet)
500 meters (1640 feet)

## Slide 9
Four Message Types
Data Frame
  Used to transmit data
Remote Frame
  Used to request data transmission
Error Frame
  Sent by a node that detects an error
Overload Frame
  Sent by a node to request a delay in transmission
CAN Message Types

## Slide 12: CAN ARBITRATION
CSMA/CA scheme is employed
All nodes must wait for an idle bus condition.
If two nodes begin transmitting simultaneously, then they participate in an arbitration process.
Wired-AND mechanism is used.
The node with the lower ID number wins the arbitration and continues transmitting its message.
The loser of the arbitration backs off and re-tries.

## Slide 19
CAN Data Protection­
•
Bit Monitoring;
- Sender’s Task
•!• Compares every bit placed on the CAN bus with the actual bus level
!• Discrepancy indicates a bit monitoring error and results in error handling
Error Detection

## Slide 20
Stuff Check
•!• Receiver Task
Compares arriving bit stream for a sequence of six homogeneous bits.
Detection of a sixth homogeneous bit indicates bit stuffing error and results in error handling

## Slide 21
Form Check
•!• Receiver Task
Comparison of the arriving bit stream with the message format
Detection of a dominant delimiter bit (CRC delimiter, ACK delimiter) or a dominant bit within EOF indicates a format error and results in error handling

## Slide 22
Cyclic Redundancy Check
•!• Receiver Task
Utilizes the arriving bit stream and generator polynomial for the Cyclic Redundancy Check defined in ISO 11898-1
Detection of a CRC error results in error handling

## Slide 23
ACK Check
•!• Sender Task
Acknowledge error (ACK error) is detected if the recessive level placed by the sender is not overwritten
Detection of an ACK error results in error handling

## Slide 24: CAN Advantages
High performance under light loads
Low cost
Reliable
Robust

## Slide 25: CAN Disadvantages
Unfair access: Node with high priority can hog the network
Starvation for some particular nodes

## Slide 26
Automotive
Military vehicles
Industrial machinery
Medical systems
Agricultural machinery
Marine control and navigation
Elevator control systems
Applications

## Slide 27: Conclusion
CAN is ideally suited in applications requiring a large number of short messages with high reliability in rugged operating environments.
Because CAN is message-based and not address­ based, it is especially well-suited when data is needed by more than one location and system-wide data consistency is mandatory.